## Slide 1: Learning Multi-granular Models of Physiology for Detection of Bleeding
Carnegie Mellon University Dr. Artur Dubrawski
Dr. Mathieu Guillame-Bert
University of Pittsburgh
Dr. Michael Pinsky
Dr. Gilles Clermont
Anthony Wertz Research Analyst Auton Lab
Carnegie Mellon University
October 3rd, 2017
Funded by: R01GM126811

## Slide 2: Questions
Given observations of a patient’s vitals can we determine whether or not the patient is bleeding?

## Slide 3: Questions
Given observations of a patient’s vitals can we determine whether or not the patient is bleeding?
If so,
  How quickly?
  How often will we get false alarms?
  How much data do we need?
  How does the a priori knowledge of a patient’s normal vitals affect our ability to detect bleeding?

## Slide 4: Questions
Given observations of a patient’s vitals can we determine whether or not the patient is bleeding?
If so,
  How quickly?
  How often will we get false alarms?
  How much data do we need?
  How does the a priori knowledge of a patient’s normal vitals affect our ability to detect bleeding?
Can we design an experiment to collect the hemodynamic data from patients before and while controlled bleeding takes place to evaluate these questions?

## Slide 5: Questions
Given observations of a patient’s vitals can we determine whether or not the patient is bleeding?
If so,
  How quickly?
  How often will we get false alarms?
  How much data do we need?
  How does the a priori knowledge of a patient’s normal vitals affect our ability to detect bleeding?
Can we design an experiment to collect the hemodynamic data from patients before and while controlled bleeding takes place to evaluate these questions?
It turns out, we can!

## Slide 6: Questions
Given observations of a patient’s vitals can we determine whether or not the patient is bleeding?
If so,
  How quickly?
  How often will we get false alarms?
  How much data do we need?
  How does the a priori knowledge of a patient’s normal vitals affect our ability to detect bleeding?
Can we design an experiment to collect the hemodynamic data from patients before and while controlled bleeding takes place to evaluate these questions?
It turns out, we can! With pigs* (* Ethical restrictions limit our ability to bleed humans, even in the name of science.)

## Slide 7: Experimental Design
Pigs are anesthetized and connected to various sensors for data collection…

## Slide 8: Experimental Design
Pigs are anesthetized and connected to various sensors for data collection, including:
  Vital sensor data (arterial, central venous, and pulmonary artery pressure, ECG, plethysmograph, SpO2) at 250Hz and SvO2 once every two seconds.
Vitals

## Slide 9: Experimental Design
Pigs are anesthetized and connected to various sensors for data collection, including:
  Vital sensor data (arterial, central venous, and pulmonary artery pressure, ECG, plethysmograph, SpO2) at 250Hz and SvO2 once every two seconds.
  Beat-to-beat LiDCO data.
LiDCO
Vitals

## Slide 10: Experimental Design
Pigs are anesthetized and connected to various sensors for data collection, including:
  Vital sensor data (arterial, central venous, and pulmonary artery pressure, ECG, plethysmograph, SpO2) at 250Hz and SvO2 once every two seconds.
  Beat-to-beat LiDCO data.
  Flotrac data every 20 seconds.
LiDCO
Flotrac
Vitals

## Slide 11: Experimental Design
Pigs are anesthetized and connected to various sensors for data collection, including:
  Vital sensor data (arterial, central venous, and pulmonary artery pressure, ECG, plethysmograph, SpO2) at 250Hz and SvO2 once every two seconds.
  Beat-to-beat LiDCO data.
  Flotrac data every 20 seconds.
They are left to rest for 30 minutes while baseline data is collected.
LiDCO
Flotrac
Vitals

## Slide 12: Experimental Design
Pigs are anesthetized and connected to various sensors for data collection, including:
  Vital sensor data (arterial, central venous, and pulmonary artery pressure, ECG, plethysmograph, SpO2) at 250Hz and SvO2 once every two seconds.
  Beat-to-beat LiDCO data.
  Flotrac data every 20 seconds.
They are left to rest for 30 minutes while baseline data is collected.
The pigs are then bled at a constant rate, either:
  5mL/min until mean arterial pressure drops below 40mmHg, or
  20mL/min until mean arterial pressure drops below 30mmHg.
LiDCO
Flotrac
Vitals
Bleed starts
5mL/min
20mL/min

## Slide 13: Computational Experimental Design
The data is featurized and those features are split into different (though not mutually exclusive) groups.
(Featurization and the groups will be discussed soon.)

## Slide 14: Computational Experimental Design
The data is featurized and those features are split into different (though not mutually exclusive) groups.
Those feature sets are used to validate random forest models that classify a pig as bleeding or not in a leave - one - pig - out cross validation framework.
(These will also be discussed briefly.)
Training Set
Testing Set

## Slide 15: Computational Experimental Design
The data is featurized and those features are split into different (though not mutually exclusive) groups.
Those feature sets are used to validate random forest models that classify a pig as bleeding or not in a leave-one-pig-out cross validation framework.
The detection results are evaluated by means of Receiver Operator Characteristic (ROC) and Activity Monitoring Operator Characteristic (AMOC) curves.
Training Set
Testing Set
ROC
AMOC
(These will be described in a bit more detail since
they’re necessary to understand the results.)

## Slide 16: Featurizations and Groups
A featurization is, simply put, a transformation of the original input data.
  E.g. given a time series of blood pressures the mean is computed every five minutes.

## Slide 17: Featurizations and Groups
A featurization is, simply put, a transformation of the original input data.
  E.g. given a time series of blood pressures the mean is computed every five minutes.
We are especially interested in time series featurizations since these are directly impacted by data granularity.

## Slide 18: Featurizations and Groups
A featurization is, simply put, a transformation of the original input data.
  E.g. given a time series of blood pressures the mean is computed every five minutes.
We are especially interested in time series featurizations since these are directly impacted by data granularity.
To assess the impact of data granularity we grouped the featurizations in four blocks:

## Slide 19: Featurizations and Groups
A featurization is, simply put, a transformation of the original input data.
  E.g. given a time series of blood pressures the mean is computed every five minutes.
We are especially interested in time series featurizations since these are directly impacted by data granularity.
To assess the impact of data granularity we grouped the featurizations in four blocks:
  Low Frequency (LF)
Low Frequency (LF) - 7 Features
Instantaneous vital data only. Assuming a low frequency of data collection (around one observation every two minutes) useful time featurizations are not possible without incurring very long detection latencies.

## Slide 20: Featurizations and Groups
A featurization is, simply put, a transformation of the original input data.
  E.g. given a time series of blood pressures the mean is computed every five minutes.
We are especially interested in time series featurizations since these are directly impacted by data granularity.
To assess the impact of data granularity we grouped the featurizations in four blocks:
  Low Frequency (LF)
  Beat-to-Beat (B2B)
Beat-to-Beat (B2B) - 158 Features Data from LiDCO device every heart beat, and data from Flotrac device every 20 seconds. Flotrac featurizations include additional features provided by Flotrac group that are not ordinarily available.
Low Frequency (LF) - 7 Features
Instantaneous vital data only. Assuming a low frequency of data collection (around one observation every two minutes) useful time featurizations are not possible without incurring very long detection latencies.

## Slide 21: Featurizations and Groups
A featurization is, simply put, a transformation of the original input data.
  E.g. given a time series of blood pressures the mean is computed every five minutes.
We are especially interested in time series featurizations since these are directly impacted by data granularity.
To assess the impact of data granularity we grouped the featurizations in four blocks:
  Low Frequency (LF)
  Beat-to-Beat (B2B)
  Beat-to-Beat + Low Frequency (B2B+LF)
Beat-to-Beat + Low Frequency (B2B+LF)
Beat-to-Beat (B2B) - 158 Features Data from LiDCO device every heart beat, and data from Flotrac device every 20 seconds. Flotrac featurizations include additional features provided by Flotrac group that are not ordinarily available.
Low Frequency (LF) - 7 Features
Instantaneous vital data only. Assuming a low frequency of data collection (around one observation every two minutes) useful time featurizations are not possible without incurring very long detection latencies.

## Slide 22: Featurizations and Groups
A featurization is, simply put, a transformation of the original input data.
  E.g. given a time series of blood pressures the mean is computed every five minutes.
We are especially interested in time series featurizations since these are directly impacted by data granularity.
To assess the impact of data granularity we grouped the featurizations in four blocks:
  Low Frequency (LF)
  Beat-to-Beat (B2B)
  Beat-to-Beat + Low Frequency (B2B+LF)
  High Frequency
High Frequency (HF) - 323 Features
Includes various featurizations of vital waveforms along with featurizations of B2B data.
Beat-to-Beat + Low Frequency (B2B+LF)
Beat-to-Beat (B2B) - 158 Features Data from LiDCO device every heart beat, and data from Flotrac device every 20 seconds. Flotrac featurizations include additional features provided by Flotrac group that are not ordinarily available.
Low Frequency (LF) - 7 Features
Instantaneous vital data only. Assuming a low frequency of data collection (around one observation every two minutes) useful time featurizations are not possible without incurring very long detection latencies.

## Slide 23: Featurizations and Groups
A featurization is, simply put, a transformation of the original input data.
  E.g. given a time series of blood pressures the mean is computed every five minutes.
We are especially interested in time series featurizations since these are directly impacted by data granularity.
To assess the impact of data granularity we grouped the featurizations in four blocks:
  Low Frequency (LF)
  Beat-to-Beat (B2B)
  Beat-to-Beat + Low Frequency (B2B+LF)
  High Frequency
We also compare models with and without baseline normalization.
High Frequency (HF) - 323 639 Features
Includes various featurizations of vital waveforms along with featurizations of B2B data.
Beat-to-Beat + Low Frequency (B2B+LF)
Beat-to-Beat (B2B) - 158 312 Features Data from LiDCO device every heart beat, and data from Flotrac device every 20 seconds. Flotrac featurizations include additional features provided by Flotrac group that are not ordinarily available.
Low Frequency (LF) - 7 14 Features
Instantaneous vital data only. Assuming a low frequency of data collection (around one observation every two minutes) useful time featurizations are not possible without incurring very long detection latencies.

## Slide 24: Individual Baseline Normalization
Patients can be very different when stable.
Stable before event.
After t=0 something
interesting starts to
happen to the signals.

## Slide 25: Individual Baseline Normalization
Patients can be very different when stable.
What threshold yields fast detection of event at t=0 and few false alarms for all patients?
Stable before event.
After t=0 something
interesting starts to
happen to the signals.

## Slide 26: Individual Baseline Normalization
Patients can be very different when stable.
What threshold yields fast detection of event at t=0 and few false alarms for all patients?
Assume some regularity in the baseline period:
  Center on the mean.
  Scale by its standard deviation.

## Slide 27: Individual Baseline Normalization
Patients can be very different when stable.
What threshold yields fast detection of event at t=0 and few false alarms for all patients?
Assume some regularity in the baseline period:
  Center on the mean.
  Scale by its standard deviation.
  Now we can find a threshold for this data the yields fast detections and few false positives.

## Slide 28: Individual Baseline Normalization
Patients can be very different when stable.
What threshold yields fast detection of event at t=0 and few false alarms for all patients?
Assume some regularity in the baseline period:
  Center on the mean.
  Scale by its standard deviation.
  Now we can find a threshold for this data the yields fast detections and few false positives.
For this to work we need to collect data when we know the patient is stable.
  Not available for every patient.
  But can be captured for patients prior to, for example, surgery.

## Slide 29: Evaluation Methodology
Separate models are trained for combinations of
  5mL/min (n=14) or 20mL/min (n=46)
  LF, B2B, B2B+LF, HF
  No normalization or Individual baseline normalized
  16 different models in total.
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Normalized
B2B - 5mL/min - Normalized
B2B+LF - 5mL/min - Normalized
HF Model - 5mL/min - Normalized

## Slide 30: Evaluation Methodology
Separate models are trained for combinations of
  5mL/min (n=14) or 20mL/min (n=46)
  LF, B2B, B2B+LF, HF
  No normalization or Individual baseline normalized
  16 different models in total.
Each model is a random forest classifier built to distinguish non-bleeding instances (before t=0) from bleeding instances (after t=0).
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Normalized
B2B - 5mL/min - Normalized
B2B+LF - 5mL/min - Normalized
HF Model - 5mL/min - Normalized
Bleeding?
Yes
No

## Slide 31: Evaluation Methodology
Separate models are trained for combinations of
  5mL/min (n=14) or 20mL/min (n=46)
  LF, B2B, B2B+LF, HF
  No normalization or Individual baseline normalized
  16 different models in total.
Each model is a random forest classifier built to distinguish non-bleeding instances (before t=0) from bleeding instances (after t=0).
Models are evaluated in a leave-one-pig-out cross validation framework.
Training Set
Testing Set
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Normalized
B2B - 5mL/min - Normalized
B2B+LF - 5mL/min - Normalized
HF Model - 5mL/min - Normalized
Bleeding?
Yes
No

## Slide 32: Evaluation Methodology
Separate models are trained for combinations of
  5mL/min (n=14) or 20mL/min (n=46)
  LF, B2B, B2B+LF, HF
  No normalization or Individual baseline normalized
  16 different models in total.
Each model is a random forest classifier built to distinguish non-bleeding instances (before t=0) from bleeding instances (after t=0).
Models are evaluated in a leave-one-pig-out cross validation framework.
Model performance is evaluated using ROC and AMOC curves.
Training Set
Testing Set
ROC
AMOC
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Non-normalized
B2B - 5mL/min - Non-normalized
B2B+LF - 5mL/min - Non-normalized
HF Model - 5mL/min - Non-normalized
LF - 5mL/min - Normalized
B2B - 5mL/min - Normalized
B2B+LF - 5mL/min - Normalized
HF Model - 5mL/min - Normalized
Bleeding?
Yes
No

## Slide 33: Purpose of the Receiver Operating Characteristic (ROC) Curve
An ROC curve characterizes the performance tradeoffs made when tuning a classifier threshold.
We generally include at least a random choice model and one or more other models we want to compare.
This is the model we want to compare with random guessing.
This model (call it “Random”) chooses a class at random with uniform probability.

## Slide 34: Purpose of the ROC Curve
An ROC curve characterizes the performance tradeoffs made when tuning a classifier threshold.
We generally include at least a random choice model and one or more other models we want to compare.
This curve characterizes the tradeoff between improving true positive rate (TPR) or false positive rate (FPR).
For a given FPR we can lookup the expected TPR.
TPR: What fraction of the positive cases did we correctly identify?
FPR: How often are we incorrectly alerting of a condition that is not really present?
(Or: How much do the nurses hate the new monitor?)

## Slide 35: Evaluating an ROC Curve
An ROC curve characterizes the performance tradeoffs made when tuning a classifier threshold.
We generally include at least a random choice model and one or more other models we want to compare.
This curve characterizes the tradeoff between improving true positive rate (TPR) or false positive rate (FPR).
For a given FPR we can lookup the expected TPR.
A better performing classifier will tend to move the curve toward the top left corner (i.e. more positive detections made with fewer false detections).
Best to be up here

## Slide 36: Low False Positive Rates on an ROC Curve
We are often most interested in the low FPR range in operation...
We want to look at this region.
Low FPR = Fewer false alarms.

## Slide 37: Low False Positive Rates on an ROC Curve
We are often most interested in the low FPR range in operation…
...so we plot FPR on the log scale to zoom in to the smaller values.
Now it’s much clearer

## Slide 38: Low False Negative Rates on an ROC Curve
The other end of the ROC is also interesting, so we want to zoom there too…
This side is interesting too…

## Slide 39: Low False Negative Rates on an ROC Curve
The other end of the ROC is also interesting, so we want to zoom there too…
…so we can invert the rates and swap the axes…
We flipped and rotated the ROC… Why?

## Slide 40: Low False Negative Rates on an ROC Curve
The other end of the ROC is also interesting, so we want to zoom there too…
…so we can invert the rates and swap their axes…
Note that:
1-FPR=TNR
1-TPR=FNR
TNR: How much time do we spend on patients who need it by avoiding too much focus on those who don’t?
FNR: How often do we miss something potentially really bad?

## Slide 41: Low False Negative Rates on an ROC Curve
The other end of the ROC is also interesting, so we want to zoom there too…
…so we can invert the rates and swap their axes…
…then plot the false negative rate (FNR) on the log scale.

## Slide 42: ROC Curve
The other end of the ROC is also interesting, so we want to zoom there too…
…so we can invert the rates and swap their axes…
…then plot the false negative rate (FNR) on the log scale.
Now we see both interesting regions clearly!

## Slide 43: Purpose of the Activity Monitoring Operating Characteristic (AMOC) Curve
Given a time series of predictor outputs generated by our model…
Interesting event
starts here

## Slide 44: Purpose of the AMOC Curve
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
You can ignore this grayed region. We can’t detect the event before it occurs.

## Slide 45: Computing an AMOC
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
How do we compute this?

## Slide 46: Computing an AMOC
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
How do we compute this?
  Call a “detection” an output greater or equal to 0.2.

## Slide 47: Computing an AMOC
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
How do we compute this?
  Call a “detection” an output greater or equal to 0.2. Assigning this threshold gives us
    A time to detection (the first true positive).

## Slide 48: Computing an AMOC
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
How do we compute this?
  Call a “detection” an output greater or equal to 0.2. Assigning this threshold gives us
    A time to detection (the first true positive).
    A number of false positives (thus, FPR).

## Slide 49: Computing an AMOC
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
How do we compute this?
  Call a “detection” an output greater or equal to 0.2. Assigning this threshold gives us
    A time to detection (the first true positive).
    A number of false positives (thus, FPR).
  Do this again for another threshold, 0.3, and now there are two points on the AMOC.
Fewer false alarms
More latency

## Slide 50: Computing an AMOC
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
How do we compute this?
  Call a “detection” an output greater or equal to 0.2. Assigning this threshold gives us
    A time to detection (the first true positive).
    A number of false positives (thus, FPR).
  Do this again for another threshold, 0.3, and now there are two points on the AMOC.
  Keep doing this for all thresholds for the complete curve.

## Slide 51: Low False Positive Rates on an AMOC
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
How do we compute this?
  Call a “detection” an output greater or equal to 0.2. Assigning this threshold gives us
    A time to detection (the first true positive).
    A number of false positives (thus, FPR).
  Do this again for another threshold, 0.3, and now there are two points on the AMOC.
  Keep doing this for all thresholds for the complete curve.
Lower FPR values are generally more operationally useful…

## Slide 52: Low False Positive Rates on an AMOC
Given a time series of predictor outputs generated by our model…
...we want to characterize the tradeoff between detection latency (time to detection) and false alarms (FPR).
How do we compute this?
  Call a “detection” an output greater or equal to 0.2. Assigning this threshold gives us
    A time to detection (the first true positive).
    A number of false positives (thus, FPR).
  Do this again for another threshold, 0.3, and now there are two points on the AMOC.
  Keep doing this for all thresholds for the complete curve.
Lower FPR values are generally more operationally useful… so we put FPR on the log scale to zoom in to this region.

## Slide 53: Missing Detections on AMOCs
When computing AMOCs using multiple time series, not all series will have a detection for every output threshold.
  If an event in a time series is not detected (i.e. zero true positives) we call that a “miss”.
  As will be shown on subsequent slides, relaxing the minimum fraction of time series that must be detected can greatly reduce detection latency at the cost of missing some detections.

## Slide 54: Aggregating AMOC Curves
When computing AMOCs using multiple time series, not all series will have a detection for every output threshold.
  If an event in a time series is not detected (i.e. zero true positives) we call that a “miss”.
  As will be shown on subsequent slides, relaxing the minimum fraction of time series that must be detected can greatly reduce detection latency at the cost of missing some detections.
The AMOCs on the next slides show the “maximum” time to detection for a given threshold.

## Slide 55: Results

## Slide 56: Understand the Legend
We’ll start with classifications results for the 5mL/min cohort. But first, the legend:

## Slide 57: Performance Improves with Increasing Granularity
ROC curves for 5mL/min bleed group
These results are for the 5mL/min cohort.
In general we see that greater data density yields better classification performance.
Better
Higher density
Lower density
Clear how much better here!
How much better at FPR of 10-3?
?

## Slide 58: Performance Improves with Normalization
ROC curves for 5mL/min bleed group
These results are for the 5mL/min cohort.
In general we see that greater data density yields better classification performance.
Knowledge of individual baselines vastly improves performance.
Better
Normalized
Non-normalized

## Slide 59: Performance is Similar Between Bleed Groups
ROC curves for 5mL/min and 20mL/min bleed groups
This is true in the
20mL/min group as well.
5mL/min
20mL/min

## Slide 60: Early Performance is Much Better with Higher Granularity
ROC curves for 5mL/min bleed group 0-5 minutes (top) vs 10-15 minutes (bottom) into the bleed
0-5 min
10-15 min

## Slide 61: Moving from the ROC to the AMOC
The ROC shows of the trade-off between correct and incorrect classifications.
What about the timeliness of a detection?

## Slide 62: Evaluating Time to Detection (Latency)
AMOC curve for 5mL/min bleed group
These results are for the 5mL/min cohort.

## Slide 63: Evaluating Time to Detection (Latency)
AMOC curve for 5mL/min bleed group
These results are for the 5mL/min cohort.
The performance is better when we move to the bottom left of the plot (lower FPR, lower latency).
Better

## Slide 64: Evaluating Time to Detection (Latency)
AMOC curve for 5mL/min bleed group
These results are for the 5mL/min cohort.
The performance is better when we move to the bottom left of the plot (lower FPR, lower latency).
This AMOC enforces the constraint that a detection is made on all pigs…

## Slide 65: Faster Detections when Minimum Detected Fraction is Lower
AMOC curves for 5mL/min bleed group
These results are for the 5mL/min cohort.
The performance is better when we move to the bottom left of the plot (lower FPR, lower latency).
This AMOC enforces the constraint that a detection is made on all pigs… but we can loosen that constraint for faster detections at the expense of some missed detections.
Faster detection
Slower detection
All bleeds detected
At least 90% of bleeds detected
≥ 80%
≥ 90%
100%

## Slide 66: Faster Detections and Fewer False Alarms with Higher Granularity
AMOC curves for 5mL/min bleed group
These results are for the 5mL/min cohort.
The performance is better when we move to the bottom left of the plot (lower FPR, lower latency).
This AMOC enforces the constraint that a detection is made on all pigs… but we can loosen that constraint for speedier detections at the expense of some missed detections.
We see that greater data density generally yields faster detections for the same FPR on normalized models.
Better
Lower density
Higher Density
≥ 80%
≥ 90%
100%

## Slide 67: Faster Detections and Fewer False Alarms with Normalization
AMOC curves for 5mL/min bleed group
These results are for the 5mL/min cohort.
The performance is better when we move to the bottom left of the plot (lower FPR, lower latency).
This AMOC enforces the constraint that a detection is made on all pigs… but we can loosen that constraint for speedier detections at the expense of some missed detections.
We see that greater data density generally yields faster detections for the same FPR on normalized models.
Knowledge of individual baselines allows faster detections for the same FPR.
Better
Non-normalized
Normalized
≥ 80%
≥ 90%
100%

## Slide 68: Detection Performance by Time Latency
Lower granularity models detect more slowly for the slower bleeding pigs.
≥ 90%

## Slide 69: Detection Performance by Time Latency
Lower granularity models detect more slowly for the slower bleeding pigs.
But the highest granularity model detects them with the same latency.
≥ 90%

## Slide 70: Detection Performance by Volume Lost
Lower granularity models detect more slowly for the slower bleeding pigs.
But the highest granularity model detects them with the same latency.
Comparing by volume of blood loss reveals earlier detections in terms of volume of blood lost for the slower bleeding cohort.
≥ 90%

## Slide 71: Detection Performance by Volume Lost
Lower granularity models detect more slowly for the slower bleeding pigs.
But the highest granularity model detects them with the same latency.
Comparing by volume of blood loss reveals earlier detections in terms of volume of blood lost for the slower bleeding cohort.
This is especially true in the case of the high frequency models.
≥ 90%

## Slide 72: Detection Performance by Time and Volume Lost
Lower granularity models detect more slowly for the slower bleeding pigs.
But the highest granularity model detects them with the same latency.
Comparing by volume of blood loss reveals earlier detections in terms of volume of blood lost for the slower bleeding cohort.
This is especially true in the case of the high frequency models.
Presence of a detectable response appears more dependent on some time delay from the onset of bleed rather than
  volume of blood lost or
  severity (5 vs 20 mL/min) of the bleeding.
≥ 90%

## Slide 73: Detection Performance by Time and Volume Lost
Lower granularity models detect more slowly for the slower bleeding pigs.
But the highest granularity model detects them with the same latency.
Comparing by volume of blood loss reveals earlier detections in terms of volume of blood lost for the slower bleeding cohort.
This is especially true in the case of the high frequency models.
Presence of a detectable response appears more dependent on some time delay from the onset of bleed rather than
  volume of blood lost or
  severity (5 vs 20 mL/min) of the bleeding.
  But seeing this requires denser data.
≥ 90%

## Slide 74: Discussion
Clinical Implications:
Our results show that we can detect bleeding quickly at a low rate of false alarms, in particular when baseline data is available. (e.g. for patients prior to surgery, soldiers, astronauts…)
Performance is improved when more granular data can be utilized, suggesting bedside monitoring equipment capable of capturing and processing higher density data can be beneficial.
What’s next?
Can models quantify the amount of blood lost?
Can we eliminate the necessity of individualized baselines?
How well can we do with non-invasive monitoring?
Can we differentiate from other disease states? (e.g. anaphylactic shock, septic shock…)

## Slide 75: The Main Take-Aways
Machine learning enables building powerful multi-variate models for bleeding detection.
Higher granularity data improves detection performance.
Knowledge of a personal baseline improves detection performance.